# SystemD mode recovery single mode linux kernel param
Parametre Kernel
- systemd.unit=rescue.target
- systemd.debug-shell=1
- systemd.unit=emergency.target
pour allez dans le tty8 ou tty9
ce qui revient à
systemctl enable debug-shell.service

## Avec init=/bin/bash (à l'ancienne)
Dans le grub, ligne commençant par linux
init=/bin/bash
mount -n -o remount,rw / passwd reboot -f

## rd.break
kernel param rd.break Si SeLinux : ajouter : enforcing=0
Exemple :
rd.break enforcing=0
Puis
loadkeys fr chroot /sysroot

## Sur RedHat
rd.break
? enforcing=0
mount -o remount,rw /sysroot chroot /sysroot passwd touch /.autorelabel # ou alors (plus rapide) : load_policy -i #puis restorecon -Rv /etc

### Alternative à touch /.autorelabel
- Remove rhgb quiet using the backspace key.
- You can change “ro” to “rw” in this grub line to avoid having to do a remount (shown below).
- IMPORTANT Add to the kernel line: rd.break enforcing=0 NOTE: you might have to make “console=tty0” above as well depending if it's virtual or not.
- Press Ctrl x to resume the boot process. NOTE: If you did not change “ro” to “rw” above, make sure to remount the /sysroot partition as shown below.
mount –o remount,rw /sysroot chroot /sysroot passwd root

- Type exit twice to continue the boot process
- Log in, open a terminal and enter the root account.
restorecon -v /etc/shadow setenforce 1 ; getenforce